ASR-2300 GNU Radio / Eclipse Installation Notes

A2300 Open Source Project

Managed Document
Document Version: 0.5 / Filename: ASR-2300 GNU Software Document.docx / Last Revised

Copyright © 2013 Loctronix Corporation
Document Control
Revision History

Revision	Date	Description	Author
R.00	9/09/2013	Initial specification draft	C. Center
R.01	9/25/2013	General updates.	C. Center

Contents
1.	Introduction	4
1.1	Intended Use	4
1.2	Related Documents	4
2.	Communications Overview	5
3.	GNU Radio	6
3.1	Installation	6
3.2	Custom Motherboard	7
3.3	Custom Daughterboard	7
3.4	Python	8
4.	USB Interfaces	9
4.1	Fedora for Cypress FX3	9
4.2	Fedora USB installation	9
4.3	USB Transport	10
5.	Eclipse	12
5.1	Linkage	12
6.	Applications	13
6.1	A2300Identify	13
Introduction
This document details the gnuradio communication interface for the ASR-2300. The ASR-2300 implements a USB communication interfaces for gnuradio. Internally, these interfaces support the Loctronix Device Communications Interface (DCI) protocol. Additionally, Loctronix provides an enhanced Loctronix Advanced Software Radio™ (ASR) platform targeting navigation applications for GPS/GNSS challenged environments.
Intended Use
The information contained in this document is the proprietary property of Loctronix Corporation. Any unauthorized use of this information and related protocols stripping prohibited. The specification is managed by Loctronix and may change without notice. Every attempt will be made to maintain backward compatibility.
This document is intended for use by Loctronix and its development partners who have authorized access to detailed design documentation for ASR and the WCA. This information is not for general circulation and requires a nondisclosure agreement before access.
Related Documents
GNU Radio
Communications Overview
GNU Radio is a free & open-source software development toolkit that provides signal processing blocks to implement software radios. It can be used with readily-available low-cost external RF hardware to create software-defined radios, or without hardware in a simulation-like environment.
GNU Radio applications are primarily written using the Python programming language, while the supplied performance-critical signal processing path is implemented in C++ using processor floating-point extensions, where available.
GNU Radio
Post Installation Notes
After installing the gnuradio package I added the following lines to .bash_profile:
export PATH
export LD_LIBRARY_PATH=/home/chris/Projects/gnuradio/src/uhd/host/build/lib
export PYTHONPATH=/usr/local/lib64/python2.7/dist-packages:/usr/local/lib64/python2.7/site-packages
We probably have to add to the LD_LIBRARY_Path our new stuff:
Loctronix generates a file called libUhdAdaptor.so. It should be placed in this directory (for 64-bit Fedora):
/usr/share/lib64/uhd/modules/libUhdAdaptor.so
If you cannot find that file, our system environment can create a Debug build and put it here:
WksAsr2300/pkgs/OpenSource/host/lib/UhdAdaptor/Debug
This section defines the details for working with the proprietary interface. The interface is intended for use via the ASR-2300 WCA driver implemented in support of the WCA platform available for Linux and Windows -based devices. The WCA driver for the ASR-2300 accesses the USB interface directly using lib-usb 1.0(Linux) or Cypress APIs (Windows), enabling high-speed bulk transfer of data between the host platform and the ASR-2300. The minimum configuration defines seven (ep0 through ep6) and points for configuration, control, and RAM operations. Additional endpoints supporting WCA ports may be defined depending on the particular FPGA logic loaded.
This section details the specific specifications for each of the endpoints and implementation considerations.
Installation
Our installation follows the gnuradio website format. The last install we used the "wget" method to automatically download the gnuradio and uhd software. You will need to have "sudo" privilages to do this[1].
[1] A simple way to verify if you have sudo privilages is to issue the command "sudo dir".
Software Installation Notes:
gnuradio source is can be downloaded from the github using the following command:
> git clone http://git.gnuradio.org/git/gnuradio.git

We installed gnuradio-0:3.6.5-2
Which version of boost am I using? (mine says 0:1.50)
> repoquery yum repository boost<CR>
gnuradio source
gnuradio/gnuradio = build directory
Refer to the gnuradio.org website for build instructions.
Build Option 1 (with manual Debug entry).
Download the gnuradio 3.7.0 or later software and perform a build on you system.
1) Edit the build-gnuradio CMAKE line to read as follows:
      CAKE_FLAG1=-g3 -O0 -DCMAKE_BUILD_TYPE=Debug
        -DPythonLibs_FIND_VERSION:STRING="2.7"
2) You may want to edit the "build-gnuradio" file and comment out the "git checkout" if you have local changes you do not want to be overwritten during the build process (since it does an automatic git update).
3) Run: ./build-gnuradio udh_build[2]
[2] You do not have to be root for this command.
Build Option 2
pwd> /home/chris/Projects/gnuradio/src/gnuradio/build
cmake -DCMAKE_BUILD_TYPE=Debug ../
make && make test

98% tests passed, 3 tests failed out of 175

Total Test time (real) = 80.61 sec

The following tests FAILED:
 4 - qa_tag_utils (Failed)
 5 - qa_feval (Failed)
 6 - qa_kludged_imports (Failed)
Errors while running CTest

Post Build Options
After installing and building the gnuradio package I added the following lines to .bash_profile (note that you may have to “source .bash_profile” after boot.
$ export LD_LIBRARY_PATH=/home/chris/Projects/gnuradio/src/uhd/host/build/lib
$ export PYTHONPATH=/usr/local/lib64/python2.7/site-packages
We probably have to add to the LD_LIBRARY_PATH with our new stuff as follows:
$ export $LD_LIBRARY_PATH:<new_stuff>
Ours is libUhdAdaptor.so and lives here:
WksAsr2300/pkgs/OpenSource/host/lib/UhdAdaptor/Debug
$ export $LD_LIBRARY_PATH:/ WksAsr2300/pkgs/OpenSource/host/lib/UhdAdaptor/Debug
Custom Motherboard
Create a new device driver when the driver in lib/usrp/ cannot support your custom FPGA or hardware modifications. Make a copy of the relevant driver code in lib/usrp/, make mods, and rename the class. The new device code should register itself into the discovery and factory system.
(see /Projects/gnuradio/src/uhd/host/lib/usrp/)
Custom Daughterboard
 Use code from an existing daughterboard in lib/usrp/dboard/* as an example. Your daughterboard code should subclass an rx dboard, rx dboard, or xcvr dboard; and it should respond to calls to get and set properties. The new daughterboard code should register itself into the dboard manager with a unique rx and/or tx 16 bit identification number.

Installation Notes (Step 1).

/home/chris/Projects/gnuradio/src

wget http://www.sbrac.org/files/build-gnuradio && chmod a+x ./build-gnuradio && ./build-gnuradio

edit .bash_profile to change
export PATH
to:
export PATH
export PYTHONPATH=/usr/local/lib64/python2.7/site-packages

source .bash_profile

UHD
Proprietary software can link to the UHD and not have to open source their code.

UHD Requirements:
> Git Account
> C++ compiler (gcc, msvc)
> CMake 2.6 (or higher)
> Boost 1.36 (or higher)
> LibUSB 1.0 (or higher)
> Python 2.6 (or higher)
> Cheetah 2.6 (or higher
> Doxygen
> Docutils
Python
This section defines a simple python example.
1. How to find a uhd device:
d = uhd.find_devices(uhd.device_addr(options.args))
uhd_type = d[0].get('type')
if( uhd_type == "asr-2300")
tr0 = uhd.tune_request(freq0)

USB Interfaces
This endpoint is a messaging type endpoint supporting configuration, command and control messages defined by the USB specification for enumerating and configuring USB devices. Message protocol supported on this interface is in compliance with USB 2.0 and 3.0 standards. Standard support implemented by the FX-3 supports endpoint 0 communications. At this time no specific modifications of this command protocol are expected.
Fedora for Cypress FX3
Run "lsusb" to get a list of USB devices on the system. Observe something like:
$ lsusb
Bus 001 Device 002: ID 8087:0024 Intel Corp. Integrated Rate Matching Hub
Bus 002 Device 002: ID 8087:0024 Intel Corp. Integrated Rate Matching Hub
Bus 003 Device 002: ID ffff:00ff
Bus 003 Device 004: ID 0781:5530 SanDisk Corp. Cruzer
Run "dmesg" to get a list of all device and see this.
$ dmesg
[ 1196.921888] usb 3-2: new high-speed USB device number 4 using xhci_hcd
[ 1196.955469] usb 3-2: New USB device found, idVendor=ffff, idProduct=00ff
[ 1196.955476] usb 3-2: New USB device strings: Mfr=1, Product=2, SerialNumber=0
[ 1196.955480] usb 3-2: Product: FX3
[ 1196.955483] usb 3-2: Manufacturer: Cypress FX3
Fedora USB installation
On Linux, Udev handles USB plug and unplug events. The following commands install a Udev rule so that a non-root user may access the device (for a UHD device):

$ cd <install-path>/share/uhd/utils
$ sudo cp uhd-usrp.rules /etc/udev/rules.d/
$ sudo udevadm control --reload-rules

After the update you can run the following command:
$ lsusb -v -d:00ff
The first few lines illustrated below indicate that you do not have permission to access the device. This will result in device open failures.
Bus 003 Device 011: ID ffff:00ff
Couldn't open device, some information will be missing
(this output indicates you do not have "driver" access.

Asr2300 Group
The udev daemon is used by some Linux distributions to handle plug/unplug events for usb devices.
Add a group: su /usr/sbin/groupadd Asr2300[3]
[3] If you have problems with this command you should change to that directory in which the command is in and run as superuser.
Add a user to the group: /usr/sbin/usermod -G Asr2300 -a chris
Create a file in the directory "/etc/udev/rules.d" and name it "99-Asr2300.rules"
ATTRS{idVendor}=="ffff",ATTRS{idProduct}=="00ff",MODE="0666",GROUP="Asr2300"
You could echo that above text for the following...
echo 'ATTR... ' > tmpFile
su root
chown root.root tmpfile
sudo mv tmpfile /etc/udev/rules.d/99-Asr2300.rules
sudo udevadm control --reload-rules (load new stuff)
lsusb | grep ffff:00ff (show you installed it ok).
Note my groups with "Asr2300" as the primary. (note that the Asr2300 matches that found in the 99-Asr2300.rules name. I had to reboot Fedora after all of this.
$ groups chris
chris : Asr2300 wheel users dialout usrp
After the driver is installed issue the command "lsusb". To see additional information use the command:
$ lsusb -v -d:00ff
More information can be found at this link (at the time of this document posting):
http://gnuradio.org/redmine/projects/gnuradio/wiki/UdevConfig
Run "lsusb" to get a list of USB devices on the system. Observe something like:
[chris@loc-wdn-dev02 ~]$ lsusb
Bus 001 Device 002: ID 8087:0024 Intel Corp. Integrated Rate Matching Hub
Bus 002 Device 002: ID 8087:0024 Intel Corp. Integrated Rate Matching Hub
Bus 003 Device 002: ID ffff:00ff
Bus 003 Device 004: ID 0781:5530 SanDisk Corp. Cruzer
Run the following command to get a list of all USB devices:

    > dmesg
The output from a typical execution is here:
[ 1196.921888] usb 3-2: new high-speed USB device number 4 using xhci_hcd
[ 1196.955469] usb 3-2: New USB device found, idVendor=ffff, idProduct=00ff
[ 1196.955476] usb 3-2: New USB device strings: Mfr=1, Product=2, SerialNumber=0
[ 1196.955480] usb 3-2: Product: FX3
[ 1196.955483] usb 3-2: Manufacturer: Cypress

USB Transport
USB Transport (LibUSB)

The USB transport is implemented with LibUSB. LibUSB provides an asynchronous API for USB bulk transfers.
Transport Parameters
The following parameters can be used to alter the transports default behavior:
recv_frame_size: The size of a single receive transfer in bytes.
num_recv_frames: The number of simultaneous receive transfers.
send_frame_size: The size of a single send transfer in bytes.
num_send_frames: The number of simultaneous send transfers.
Eclipse
Eclipse software build for a simple application (no gnuradio).
The gnuradio eclipse project "workspace" is here:
"/home/chris/Projects/WksAsr2300/pkgs/OpenSource/host/".
This project includes the Directories of:
A2300Identify
A2300Usb
Common
UhdAdaptor
Creators of custom hardware can create drivers that use the UHD API. These drivers can be built as dynamically loadable modules that the UHD will load at runtime.
For a module to be loaded at runtime, it must be "either":
Found in the UHD_MODULE_PATH environmental variable
Installed into the “/usr/local/lib64/uhd/modules” directory (linux).
Installed into the “<prefix>/share/uhd/modules” directory
Linkage
Specify the following libraries:
Uhd
boost_system
boost_program_options
dl

Specify the following Library Paths:
/../Common/Debug
/home/chris/Projects/gnuradio/src/uhd/host/build/lib

Python Linkage Test
To ensure that the python setup is correct in the following python command (this will also verify that the PYTHONPATH is correct):
$python
>>> from gnuradio import gr
Applications
This endpoint provides bulk transfer of data to a specific location in memory. Each operation specifies a beginning and number of 16 bit words to be transferred. Details of how this exactly is done will be specified in a later version of this document. Memory operations will require a DCI property message to set up memory transfer operation and then this endpoint to write bulk data to the specified memory locations. Writing continues until the specified number of 16-bit words are written.
A2300Identify
This project requires you to a) run as root and b) identify the library location as follows:
> Under Eclipse | Run | Run Configurations:
1. Select C/C++ Application.
2. Select the "Environment" Tab
3. Enter a variable called "LD_LIBRARY_PATH"
4. Add a value to the library location, for example:
/home/chris/Projects/WksAsr2300/pkgs/OpenSource/host/lib/A2300Usb/Debug/

Examples
Example 1
This program scans your system for supported devices and prints out an enumerated list of discovered devices and their addresses. This UHD command will display the A2300 device information.
# uhd_find_devices --args="type=usrp1"
or
# uhd_find_devices --args="name=ASR-2300"
Example 2
Find out what "uhd" commands are available:
# from gnuradio import uhd
# dir(uhd)

Errors
This endpoint provides bulk transfer of data to a specific location in memory. Each operation specifies
Error	Resolution
Python import error: "No module named gnuradio"	Reinstall "gnuradio"
fatal error:gnu/stubs-32.h	Install gnu 32-bit support (Fedora) sudo yum install glibc-devel.i686[4]
Python Error: / >>> from gnuradio import uhd / Error: EnvironmentError: OSError: dlopen failed to load "/usr/local/lib64/uhd/modules/libUhdAdaptor.so	Eclipse environment issue. Rebuild libUhdAdaptor.so with "Common" and "uhd" libraries.
[4] The 32-bit build under 64-bit fedora is not supported by Boost (so avoid if using 64-bit fedora)